## Slide 1
EG5066 Energy Technologies: current issues & future directions
Natural Gas

## Slide 2
Natural Gas
Consists primarily of methane (CH4) but sometimes contains significant quantities of:
Ethane
Propane
Butane
Pentane
And CO2, nitrogen, helium and H2S
Found associated with crude oil
Isolated natural gas reservoirs
In coal beds – coal bed methane
As methane clathrates
Created by methanogenic organisms in marshes, bogs and landfills
EG5066 Energy Technologies: current issues & future directions

## Slide 3
Produced commercially from oil fields & natural gas fields
Sour gas, tight gas, shale gas and coal bed methane
An important fuel source
Major feedstock for fertilisers
A potent greenhouse gas
Natural Gas
EG5066 Energy Technologies: current issues & future directions

## Slide 4
Components of Natural Gas
Methane (CH4)
Ethane (C2H6)
Propane (C3H8)
Normal butane (n-C4H10)
Isobutane (i-C4H10)
Pentanes
Acid gases – CO2, H2S, mercaptans – methanethiol (CH3SH) and ethanethiol (C2H5SH)
Other gases – Nitrogen (N2) and Helium (He)
Water – water vapour and liquid water
Some natural gas condensate (aka casinghead gasoline or natural gasoline)
Crude oil
Mercury
EG5066 Energy Technologies: current issues & future directions

## Slide 5
Types of Raw Natural Gas Wells
Crude oil wells – known as associated gas either:
Separate
Dissolved in crude oil
Natural gas from gas wells & from condensate wells with little or no oil – known as non-associated gas
Condensate wells produce raw natural gas & very low density liquid hydrocarbon – natural gas condensate
EG5066 Energy Technologies: current issues & future directions

## Slide 6
EG5066 Energy Technologies: current issues & future directions
Natural Gas Condensates
A low density mixture or hydrocarbon liquids present as gaseous components in raw natural gas
Condense out if temperature reduced below hydrocarbon dewpoint temperature of raw gas
Each wet gas field has its own unique gas condensate composition:
  H2S
  Mercaptans
  CO2
  Straight chain alkanes (C2 – C12)
  Cyclohexanes
  Aromatics (benzene, toluene, xylenes, ethylbenzene)

## Slide 7
EG5066 Energy Technologies: current issues & future directions
Natural Gas Condensates
Separation technique
Raw gas cooled below hydrocarbon dewpoint
Gas condensates condense out
The condensates passed through high pressure separator where water and raw natural gas separated
Condensates passed to lower pressure vessel and flash vaporised

## Slide 8
Condensate and water removal
Tail Gas Treating
Scot process
Clauspol process
Others
Sulphur Unit
Claus process
Acid gas removal
Amine treating
Benfield process
PSA Unit
Sulphinol process
Dehydration
Glycol unit
PSA unit
Nitrogen Rejection
Cryogenic process
Absorption processes
Adsorption processes
Mercury Removal
Mol Sieves
Activated carbon
Sweetening units
Merox process
Sulphrex process
Mol sieves
Fractionation Train
De-ethanizer
De-propanizer
De-butanizer
NGL Recovery
Turbo-expander
De-methanizer
Ethane
Propane
Butanes
Pentanes
Gas Pipeline
Incinerator
Elemental Sulphur
Condensate to oil refinery
Waste water
Acid Gas
Tail Gas
Nitrogen-rich Gas
Raw Gas
Raw Gas
Flow Diagram - Natural Gas Processing Plant
Removes mercaptans
Removes H2S & CO2
EG5066 Energy Technologies: current issues & future directions

## Slide 9
World’s largest reserves located in Russia
4.757 x 1013 m3 (1.6 x 1015 cu ft)
World’s largest natural gas producer - Gazprom
World’s largest gas field
North Field – offshore Qatar
25 trillion cubic metres (9.0 x 1014 cu ft) gas in place
2nd largest
South Pars Gas Field, Iran
8 – 14 trillion cubic metre (2.8 – 5.0 x 1014 cu ft)
EG5066 Energy Technologies: current issues & future directions
Natural Gas - reserves

## Slide 10
EG5066 Energy Technologies: current issues & future directions
Natural Gas – producing countries

## Slide 11: Proved natural gas reserves at end 2007
Source: BP
EG5066 Energy Technologies: current issues & future directions

## Slide 12: Distribution of proved natural gas reserves
Source: BP
EG5066 Energy Technologies: current issues & future directions

## Slide 13: Distribution of proved gas reserves
EG5066 Energy Technologies: current issues & future directions

## Slide 14: Gas production/consumption by region
EG5066 Energy Technologies: current issues & future directions

## Slide 15: Gas reserves-to-production (R/P) ratios
EG5066 Energy Technologies: current issues & future directions

## Slide 16: Chart of gas prices
EG5066 Energy Technologies: current issues & future directions

## Slide 17: Gas consumption per capita
EG5066 Energy Technologies: current issues & future directions

## Slide 18: Major gas trade movements