## Slide 1
EG5066 Energy Technologies: current issues & future directions
Synthetic Fuels

## Slide 2
Synthetic Fuels
Synthetic fuels - liquid fuel obtained from:
Coal
Natural gas
Biomass
Worldwide production capacity July 2009 240,000 bpd (38,000 m3/day)
Direct conversion of coal to synthetic fuel originally developed in Germany
Bergius process patented in 1913 – production began in 1919
Indirect coal conversion (gasified then converted) developed in Germany by Fischer & Tropsch 1923
Number of processes – three broad categories
  Indirect
  Direct
  Biofuel
EG5066 Energy Technologies: current issues & future directions

## Slide 3
Synthetic Fuels
Commercialisation
Sasol – leading company based in South Africa
Indirect Fischer Tropsch plants:
Mossgas and Secunda CTL (160,000 bpd) in South Africa
Oryx GTL in Qatar – 35,000 bpd
Shell Bintulu in Malaysia GTL – 14,500 bpd
Mobil process plant in New Zealand
Shell Bintulu GTL plant
Mossgas
Oryx GTL
EG5066 Energy Technologies: current issues & future directions

## Slide 4
Synthetic Fuels
Indirect conversion
Most widely deployed technology
Worldwide production 260,000 bpd (41,000 m3/d) – 2009 figures
Process in which biomass, coal or natural gas converted into syngas (H2 + CO) through gasification or steam methane reforming and syngas processed to appropriate transport fuel
Known as:
  Coal to Liquids (CTL)
  Gas to Liquids (GTL)
  Biomass to Liquids (BTL)
Primary technologies:
  Fischer-Tropsch synthesis
  Mobil process (or Methanol to Gasoline – MTG)
Can also be used to produce hydrogen for fuel cells
EG5066 Energy Technologies: current issues & future directions

## Slide 5
Indirect Conversion to Synthetic Fuels
Coal
Biomass
Natural Gas
Gasification
Steam Methane Reformation
Syngas Cleanup
Fischer Tropsch Conversion
Wax Hydrocracking
Diesel Fuel
Jet Fuel
Methanol Synthesis
Methanol to Gasoline conversion (Mobil Process)
Gasoline
Syngas (H2 & CO)
Syngas (H2 & CO)
EG5066 Energy Technologies: current issues & future directions

## Slide 6
Gas to Liquids
Gas to liquids
A refinery process to convert natural gas or other gaseous hydrocarbons into longer chain hydrocarbons such as gasoline or diesel fuel
Methane-rich gases are converted into liquid fuels either via direct conversions or via syngas as an intermediate
  Fischer Tropsch process
  Mobil process
EG5066 Energy Technologies: current issues & future directions

## Slide 7
GTL Fischer-Tropsch Process
Partial oxidation of methane to CO2, CO, H2, H2O
CO to H2 ratio adjusted with Water Gas Shift Reaction
Excess CO2 removed by aqueous solution of alkanolamine
Water removed
Produces syngas (CO + H2)
Syngas reacted over iron or cobalt catalyst to give liquid hydrocarbons
Air separation
Gas Processing
Gas Synthesis
Fischer-Tropsch Process
Cracking
Air
Natural Gas
Liquid Gas
Methane
Oxygen
CO
H2
Liquid Hydrocarbons
Diesel
Naphtha
Paraffin
EG5066 Energy Technologies: current issues & future directions

## Slide 8
GTL Process
EG5066 Energy Technologies: current issues & future directions
Natural Gas
Processing
Syngas
Generation
Hydrocarbon
Synthesis
Fuel Upgrading
& Distillation
Natural
Gas
Methane
Syngas
Wax
Liquid
fuels
Hydrogen
Heat Recovery
Oxygen
Steam
NGL Fractionation
& Impurity Removal
Treatment to remove impurities
Reforming of natural gas to give syngas
Fischer-Tropsch conversion to produce hydrocarbon waxes
Upgrading to clean diesel fuel
Typical yield – 70% diesel fuel, 25% naptha
10mcf natural gas gives 1 barrel of output

## Slide 9
Source: www.sasol.com
Sasol Slurry Phase Distillate Processtm
EG5066 Energy Technologies: current issues & future directions

## Slide 10
Chevron & Nigerian National Petroleum Corporation
GTL plant at Escravos – start up 2013
325 mcf pd of natural gas converted to 33,000 bpd of low sulphur diesel fuel
EG5066 Energy Technologies: current issues & future directions

## Slide 11
Mobil Process
Developed by Mobil in early 1970s
Conversion of natural gas to syngas
Conversion of syngas to methanol
Methanol polymerised into alkanes over a zeolite catalyst to give gasoline
Steam reforming: CH4 + H20
CO + 3H2
Methanol from methane (natural gas)
Water shift reaction: CO + H2O
CO2 + H2
Synthesis: 2H2 + CO
CH3OH
Methanol dehydrated to dimethyl ether
2CH3OH
CH3OCH3 + H2O
Dehydrated over a zeolite catalyst to give gasoline
Methanol converted to gasoline by Mobil process
EG5066 Energy Technologies: current issues & future directions

## Slide 12
Direct conversion
Two processes:
Pyrolysis & Carbonisation
Hydrogenation
Synthetic Fuels
Pyrolysis & Carbonisation Processes
Carbonisation through pyrolysis or destructive distillation
Gives ; condensable coal tar, oil and water vapour, non-condensable synthetic gas and char
Condensable coal tar and oil processed by hydrogenation to remove sulphur and nitrogen
Processed to fuels
EG5066 Energy Technologies: current issues & future directions

## Slide 13
Synthetic Fuels
EG5066 Energy Technologies: current issues & future directions
Karrick Process
Invented by Lewis Karrick in late 1920s
Retort based on Nevada-Texas-Utah retort used for shale oil extraction
Coal heated with superheated steam in absence of air to 360o – 750oC.
Coal mainly used but can use oil shale or lignite
Optimizes production of lighter hydrocarbons
Generates no CO2
Unlikely to yield economically viable volumes of liquid fuel
1 tonne coal yields:
  0.175 m3 oils
  95m3 gas
  750kg semi-coke

## Slide 14
Coal to Liquids
Hydrogenation processes
Bergius process
Developed by Friedrich Bergius in 1913 – Nobel Prize for Chemistry 1931
Synthetic fuel by hydrogenation of high volatile bituminous coal
Developed before the Fischer-Tropsch method
One of main methods for Coal-to-Liquids
Coal liquefied by mixing it with hydrogen gas and heating
Dry high-volatile bituminous coal is mixed with heavy oil recycled from the process with a catalyst (tungsten or molybdenum)
Reaction at 400oC to 500oC and 20-70MPa hydrogen pressure
97% conversion rate
Used in Germany WWII, now 4000 tpd plant in China
Basis for a number of different developments
nC + (n + 1)H2
CnH2n+2
EG5066 Energy Technologies: current issues & future directions

## Slide 15
Coal to Liquids
EG5066 Energy Technologies: current issues & future directions
Hydrogenation processes
Number of different developments:
Nedol Process
Developed 1970 – 1980 by group of Japanese companies
Coal mixed with solvent and iron-based catalyst
Reactor operates at 430 – 465oC, 15 – 200 bar
Produces low quality oil
Needs upgrading
Other process include:
Gulf Oil’s Solvent refined coal
Exxon Donor solvent process
Imhausen High Pressure Process
Conoco Zinc Chloride Process
Chevron Coal Liquefaction Process

## Slide 16
Gas to Liquids
GTL Jet Fuel
Shell developed and produced 50-50 blend of synthetic GTL kerosene and conventional oil-based kerosene fuel
Gives lower SO2 and particulates emissions than conventional oil-based kerosene
EG5066 Energy Technologies: current issues & future directions
Shell’s Pearl GTL plant in Qatar
1.6 bcf pd of gas from the North Field converted to 140 kbo/d liquid fuels
Uses Shell Middle Distillate Synthesis (SMDS)

## Slide 17
Flightpaths for Aviation Biofuels
EU programme
2 million tonnes of aviation biofuels by 2020:
  Mainly based on Neste hydrogenated vegetable oil technology
  Potential 400,000 t/a F-T SPK by 2020
  Potential 100,000 t/a HPO
  Potential 160,000 t/a from algal oil
  Gives 1% replacement of global aviation kerosene by 2020
Aviation Biofuels
HRJ/HEFA – Hydroprocessed esters & fatty acids
FT-SPK – Fischer Tropsch synthetic paraffinic kerosene
ATJ – Alcohol to Jet
PTJ/HPO – Pyrolysis oil to jet/Hydrogenated pyrolysis oil
FRJ – Fermented renewable jet
USDA – Farm to Fly programme
One million gallons of biofuel per year by 2018
EG5066 Energy Technologies: current issues & future directions

## Slide 18
Gasification
Fischer-Tropsch synthesis
Hydrocracking & separation
O2
Ligno-
Cellulose
CO + 2H2
Synthesis gas
Cleaning & Conditioning
Olefins, naphtha, long chain paraffins
Jet fuel
Long chain paraffins
Hydrocracking & separation
Hydrotreating
Bio-derived oil
Jet fuel
F-T process*
HRJ*
Routes to SPK
*ASTM Approved as 50:50 mix with Jet-A
EG5066 Energy Technologies: current issues & future directions

## Slide 19
Alcohol to Jet
Aviation Biofuels
Utilises Oligomerization – process of “building C chains”
Alcohol
Ethanol Dehydration
Oligomerization
Distillation
Hydrogenation
Jet Fuel
EG5066 Energy Technologies: current issues & future directions

## Slide 20
Emerging Processes – Alcohol to Jet (ATJ)
Aviation Biofuels
Cobalt Technology with Albemarle Corp & NAWCWD
Bio n-Butanol to JP-8
Tested 50:50 in A-10 Thunderbolt II Engine
Woody biomass
N-butanol
1-butene
Oligomerization
Distillation
Hydrogenation
Jet Fuel
Fermentation
EG5066 Energy Technologies: current issues & future directions

## Slide 21
Lanza Tech
CO from SynGas (CO & H2) or offgas from steel works
Fermentation (Clostridia sp) to alcohols (ethanol, butanol, propanol)
Emerging Processes – Alcohol to Jet (ATJ)
Thermo-biological processes
Aviation Biofuels
LanzaTech with Swedish Biofuels
Swedish Biofuels technology
Alcohols to Jet Fuel
Source: Yikrazuul, 2010
Wood Ljungdahl Pathway
Reductive acetyl-CoA pathway
Methanogens or acetogenic organisms
H2 as electron donor (Energy Source)
CO2 as electron acceptor (Carbon Source)
CO2 reduced to CO
CO converted to acetyl coenzyme A
Source: Swedish Biofuels AB
C2-C5 sugars
C4-C20 Hydrocarbons
EG5066 Energy Technologies: current issues & future directions

## Slide 22
Life cycle analysis of different fuels

## Slide 23
Methanex, New Zealand. A Mobil process plant producing 5,200 t methanol a day
Synthetic Fuels
EG5066 Energy Technologies: current issues & future directions